## Slide 1: Interacting Multiple Model (IMM): Algorithm for Mode Detection & Filter Fusion
Oren Miller & Alex Rist
04/09/2025

## Slide 2: Agenda
Project Overview
Kalman Filter Review
Interacting Multiple Model (IMM)
  Overview
  Algorithm
  Example
Model Definitions
Trajectory Generation
Results
  Constant Velocity – Constant Turn Rate IMM
  Constant Velocity – Constante Turn Rate – Constant Acceleration IMM
Future Steps
Questions

## Slide 3: Project Overview
Goal: To research and implement an Interacting Multiple Model (IMM) algorithm for mode detection and fusion of multiple Kalman Filter outputs
Two trajectories will be simulated along with position and velocity measurements:
  1) Constant Velocity Constant Turn Rate Constant Velocity
  2) Constant Velocity Constant Turn Rate Constant Acceleration
Each trajectory’s designed IMM will be evaluated based on mode detection and state error

## Slide 4: Kalman Filter Review
First developed in1958 by Rudolph Kálmán. [1]
The Kalman filter is an optimal filter for LTI systems that is applicable to many estimation and navigation practices.
Consists of two primary steps:
  Time Update:
    Model based propagation of all states, under known inputs.
  Measurement Update:
    Measurement Correction of the propagated model states.
Measurement Update:
Compute Kalman Gain:
Compute Error Covariance for Updated Estimate:
Time Update:

## Slide 5: Interacting Multiple Model
First Proposed by H.A.P. Blom in 1984. [2]
Proposed as a high-efficiency solution to estimation of processes with Markovian coefficients.
  Processes where the parameters evolve according to a Markov process.
Utilizes multiple models to propagate the system and based on the innovations of each model the best update is selected and mixed with the other outputs.
This allows for complex dynamics to be estimated with various simple kinematic models.
[2]

## Slide 6: Basics Of Interacting Multiple Model
Markov Chain: Probability of the future state possibilities of a system based on current knowledge of the state
Walk
Stop
Run
0.95
0.04
0.01
0.95
0.03
0.02
0.95
0.025
0.025

## Slide 7: Basics Of Interacting Multiple Model
Markov Chains:
Walk
Stop
Run
0.95
0.04
0.01
0.95
0.03
0.02
0.95
0.025
0.025
0.95 | 0.04 | 0.01
0.025 | 0.95 | 0.025
0.01 | 0.03 | 0.95
Markov Chain Matrix

## Slide 8: Basics Of Interacting Multiple Model
Markov Chains:
Bayes Rule
  Probability of posterior given prior
Marginalization
Prior
Likelihood
Walk
Stop
Run
0.95
0.04
0.01
0.95
0.03
0.02
0.95
0.025
0.025

## Slide 9: Basics Of Interacting Multiple Model
Markov Chains:
Bayes Rule
  Probability of posterior given prior
Marginalization
Prior
Likelihood
Walk
Stop
Run
0.95
0.04
0.01
0.95
0.03
0.02
0.95
0.025
0.025
Total Probability Theorem

## Slide 10: Interacting Multiple Model Algorithim
Step Interaction
  Kalman Filter State and Covariance Estimate Updated by a Conditional Model Probability
  Goal is to mix Kalman Filter States such that the model possibilities doesn’t grow exponentially
Model Probability Update
  Model Probability Updated using the likelihoods from the Kalman Filter Bank
  Conditional Model Probability Created
State Estimate Combiner
  Kalman Filter Bank Measurement Updates are Combined with New Model Probability
  One State and Covariance Estimate
KF
State Interaction
Measurement
Model Probability Update
State Estimate Combiner

## Slide 11: Interacting Multiple Model Example
State Interaction
Kalman Filter #1
Time Update
Measurement Update
Kalman Filter #2
Time Update
Measurement Update
Meas.
Model Probability Update
State Estimate Combiner

## Slide 12: Interacting Multiple Model Example
State Interaction
Kalman Filter #1
Time Update
Measurement Update
Kalman Filter #2
Time Update
Measurement Update
Meas.
Model Probability Update
State Estimate Combiner
 | Mixed Model State Estimate | 
 | Mixed Model Covariance Estimate | 
 | Likelihood | 
 | Model Probability | 
 | Conditional Model Probability | 
 | State Estimate of IMM | 
 | Model Probability Estimate Priori | 
 | Mixed Model State Estimate | 
 | Mixed Model Covariance Estimate | 
 | Likelihood | 
 | Model Probability | 
 | Conditional Model Probability | 
 | State Estimate of IMM | 
 | Model Probability Estimate Priori | 
 | Kalman Filter Innovation Covariance
 | Kalman Filter Innovation
 | Kalman Filter Innovation Covariance
 | Kalman Filter Innovation

## Slide 13: Model Modes
Constant Velocity (CV)
Constant Turn Rate (CT)
Constant Acceleration (CA)
System States:
*NOTE: This model assumes (turn rate) is known or estimated*

## Slide 14: Trajectory Generation
CV-CT
CV-CT-CA

## Slide 15: Constant Velocity – Constant Turn Rate IMM

## Slide 16: Results (CV-CT) - Errors
Performance of IMM CV-CT Filter:

## Slide 17: Results (CV-CT) – Mode Probability
IMM Model Mode Prediction:

## Slide 18: Results (CV-CT) - Errors
Comparison of IMM CV-CT Filter:

## Slide 19: Results (CV-CT) – Effect of Incorrect Turn Rate
0
Turn Rate Error

## Slide 20: Constant Velocity – Constant Turn Rate – Constant Acceleration IMM

## Slide 21: Results (CV-CT-CA) - Errors
Performance of IMM CV-CT-CA Filter:

## Slide 22: Results (CV-CT-CA) – Mode Probability
IMM Model Mode Prediction:

## Slide 23: Results (CV-CT-CA) – Error Comparison
Comparison of IMM CV-CT-CA Filter:

## Slide 24: Future Steps
Implement IMM with a non-linear measurement model (ranges & range rates)
GPS/INS implementation
Real vs. Simulated trajectories and measurements
Increased complexity in model selection (Adding Vehicle Dynamic Model)

## Slide 25: Questions?

## Slide 26: References
Kalman, R. E. (March 1, 1960). "A New Approach to Linear Filtering and Prediction Problems." ASME. J. Basic Eng. March 1960; 82(1): 35– 45. https://doi.org/10.1115/1.3662552
Blom, Henk. (1984). An efficient filter for abruptly changing systems. Proceedings of the 23rd IEEE Conference on Decision and Control. 656 - 658. 10.1109/CDC.1984.272089.

## Slide 27
https://www.youtube.com/watch?v=pqxICLvcYlE

## Slide 28: Results (CV-CT) – Effect of Incorrect Turn Rate
0
| Turn Rate Error |